## Slide 1: Lab3
Lee Chung Lai (Bertram Lee)

## Slide 2: Single Cycle

## Slide 3: Design choices
Two write back ports
  Two registers that go along the pipeline
Comparison of BNE during ID stage (early detection, less penalty for wrong prediction)
  Add a not equal comparison block in ID stage
Some control signals for LA instruction is not available until EX stage
  Modify control signals in the control bus in EX stage

## Slide 4: Signal and Datapath naming
Controls
  normal controls: c_[stage]_[signal name]
  hazard controls: hc_[stage]_[signal name]
Datapath
  [stage]_[data path name]
c_mem_write
ex_result

## Slide 5: IF stage

## Slide 6: ID stage

## Slide 7: EX stage

## Slide 8: Forwarding, Hazards and Static Prediction
Forwarding
  No changes if writing into $0
  Forwarding unit to EX stage (Forward from MEM and WB stage)
  Forwarding unit to ID stage for BNE (same module as the one in EX stage)
Hazard (Load Use Hazard)
  Hazard Detection Unit controls stalling
    Gets input from controls of both EX stage and MEM stage
Branch Prediction
  Static Prediction (default no branch)
  Flush when incorrect prediction

## Slide 9: Forwarding and Load Use Hazard
Is the data available?
Instructions that writes to write port 1
Instructions that writes to write port 2
 | EX | MEM | WB
LW | NA | NA | A
ADD | NA | A | A
SLRi | NA | A | A
LA | NA | NA | A
 | EX | MEM | WB
LA | NA | A | A

## Slide 10: Considerations for BNE
Forwarding is same as others
Additional requirements to prevent Load Use Hazard (stalling)
  BNE does compare in ID stage, it needs data immediately in ID stage
  Unlike other instructions, when BNE is in ID stage, it needs to check data dependency in both EX stage and MEM stage
IF | ID | EX | MEM | WB
 | ADD |  | LW | 
IF | ID | EX | MEM | WB
 |  | ADD |  | LW
IF | ID | EX | MEM | WB
 | BNE |  | LW | 
IF | ID | EX | MEM | WB
 | BNE |  |  | LW

## Slide 11: Why Two Forwarding Unit?
Only one forwarding unit in EX stage
  BNE can only be determined at EX stage and need to flush two stages
Only one forwarding unit in ID stage
  Stall even for Non BNE instruction RAW dependency
Having two forwarding unit allows early branch detection and minimize stalling
IF | ID | EX | MEM | WB
 | ADD | ADD |  | 
IF | ID | EX | MEM | WB
 | ADD |  | ADD | 

## Slide 12: Testing
IF | ID | EX | MEM | WB
LW | BNE $2,$1 | $2<-mem[1] | $1<-mem[0] | 

## Slide 13
IF | ID | EX | MEM | WB
$3<-mem[2] | BNE $2,$1 | nop | $2<-mem[1] | $1<-mem[0]

## Slide 14
IF | ID | EX | MEM | WB
$3<-mem[2] | BNE $2,$1 | nop | nop | $2<-mem[1]

## Slide 15
IF | ID | EX | MEM | WB
FFFF | BNE $3,$4 | $4<-mem[3] | $3<-mem[2] | BNE $2, $1

## Slide 16
IF | ID | EX | MEM | WB
FFFF | BNE $3,$4 | nop | $4<-mem[3] | $3<-mem[2]

## Slide 17
IF | ID | EX | MEM | WB
FFFF | BNE $3,$4 | nop | nop | $4<-mem[3]

## Slide 18
IF | ID | EX | MEM | WB
$1<-mem[0] | nop | BNE $3,$4 | nop | nop

## Slide 19: Test 2

## Slide 20: Max Freqency
12-0.9 = 11.1 ns
Max frequency = 1/(11.1ns) = 90.1MHz